## Slide 1
CNENGR506
Intelligent System Control
Welcome to …

## Slide 2: CNENGR506 Intelligent System Control
Contents
Part 1 – Terminology and Objectives of Control
Part 2 – Discrete–Time Transfer Function Models
Part 3 – System Identification
Part 4 – Discrete–Time Control & Pole Assignment
Part 5 – State Variable Feedback
Part 6 – Additional Topics & Case Studies

## Slide 3: ENGR406 (506) Intelligent System Control
Contents
Part 1 – Terminology and Objectives of Control
Part 2 – Discrete–Time Transfer Function Models
Part 3 – System Identification
Part 4 – Discrete–Time Control & Pole Assignment
Part 5 – State Variable Feedback
Part 6 – Additional Topics & Case Studies

## Slide 4
Part 1 – Terminology and Objectives of Control
Contents
Section 1.1 – Introduction
Section 1.2 – Syllabus
Section 1.3 – Feedback
Section 1.4 – Control Objectives
Notes: Introduction
Course content what we cover and what we not:
Open loop basics and Closed loop-Feedback
4 basic control objectives

## Slide 5
CNENGR506)
1.1 Introduction

## Slide 6: Educational Aims
Introduction to modern algorithmic, computer-aided control system design methods.
Advanced concepts such as digital and optimal control are introduced using algebra and block diagrams.
Addresses the needs of students who would like to advance their knowledge of automatic control, optimisation and data analysis.
Practical worked-examples from robotics, industrial control, environmental systems, among other areas.

## Slide 7: “Control”
Human controls the car, direction and speed
Human also considers wider issues such as safety, fuel, navigation
Automatic control systems include power steering, cruise control, active suspension, etc.
Notes: Why I put Control on Heading: Its English common word
Lot of control here in this pic
From Human to technology
Human- 3 D control: Input break, accelerator, steering etc: Output: control output: Car speed, Road position: looks like closed loop control responding to environment
Car- may be Automatic Control: power steering,
Traffic light another control system

## Slide 8: Automatic Control
Multivariable aircraft control systems decouple flight variables such as pitch, velocity, altitude
Optimal controllers ensure the completion of the system objectives and the minimization of a performance index
https://en.wikipedia.org/wiki/Airbus_A320_family#/media/File:Airbus_A 320-100_Air_France_(AFR)_F-GFKQ_-_MSN_002_(10655931213).jpg

## Slide 9: Selected Projects
Illustrative fourth year MEng team projects and MSc individual projects…

## Slide 10
Robotics and Autonomous Systems (RAS)

## Slide 11: Environmental Control
Optimisation, control of micro–climate and energy management
(Charles Carter Building)
Control of LEDs, temperature and ventilation rate in an enclosed grow–cell

## Slide 12
Control Engineering Definition
Control Engineering is the science of changing the dynamical behaviour of physical systems in some desirable way.

## Slide 13: Module Scope
Have you been taught these?
Classical control, continuous-time, Laplace Transforms, mechanistic models, frequency domain techniques, root locus, proportional-integral-derivative (PID) control.

## Slide 14: Mass–Spring–Damper
2 x  Ku(t)
x  2
dt 2
2
n dt
dx  
d
n
x  C dx  K x  1 F (t)
dt 2
2
M dt M M
d
Ms2  Cs  K
1
X (s) 
F (s)
Notes: 1st equation- 2nd order differential equation
2nd: mathematical model
3rd: Laplace Transform

## Slide 15
PID Algorithm
dt
de(t)
e(t) dt  k
e(t)  k
u(t)  k
d
I 
p

## Slide 16
Part 1 – Terminology and Objectives of Control
Contents
Section 1.1 – Introduction
Section 1.2 – Syllabus
Section 1.3 – Feedback
Section 1.4 – Control Objectives
Section 1.5 – Module Details

## Slide 17: Module Scope (2)
Have you been taught these?
Classical control, continuous-time, Laplace Transforms, mechanistic models, frequency domain techniques, root locus, proportional-integral-derivative (PID) control.
What about these ?
Modern control methods, discrete-time, data-based (statistical) models, state variable feedback, predictive and optimal control, etc.

## Slide 18: Quick History Lesson

## Slide 19: Float Valve
float
fill valve
lift arm
tank fill tube
bowl fill tube
flush valve flapper
overflow tube
flush handle
chain
fill line
fill valve shaft
flush tube
https://en.wikipedia.org/wiki/Ballcock#/media/File:Gravity_t oilet_valves_handle_released.svg

## Slide 20: Watt’s Flyball Governor
Invented in 1788 by James Watt to regulate the admission of steam into his steam engine cylinder(s)
James Clerk Maxwell’s famous paper On Governors appeared in 1868
http://rspl.royalsocietypublishing.org/content/16/270

## Slide 21: History Lesson Continued
Mechanical controllers (float valve etc.)
Feedback dynamics (Maxwell 1868, Routh 1877 etc.)
Graphical methods based on frequency response (Nyquist 1932, Bode 1940, etc.)
Industrial process control using PID methods
… Classical Control
Numerical solution of differential equations using digital computers
R.E. Kalman (1960s), state space, moon landings
… Modern Control

## Slide 22: Classical Control
Usually PI or PID control structure
Control parameters tuned using Rules of Thumb
Bode Plots, Nyquist Diagrams etc.
Design usually based on continuous-time techniques, with the controller digitised to operate on a modern computer
Advantages: familiar to industry
Why change something that works?

## Slide 23: Modern Control
Many types of controller structure
Control gains determined on the basis of a model
e.g. model-predictive control (MPC)
Advantages: improved performance, can be optimised to meet multiple objectives, adaptive control, multivariable decoupling, etc.

## Slide 24: Syllabus
Introduction to “Modern Control” Theory
State variable feedback using non-minimal state space models
CORE TOPIC
Optimal control
Robust control
Stochastic control
Feed-forward control
Multivariable & Non-linear
Concept of Feedback, Terminology and Objectives of Control
Transfer Functions represented using the
Backward Shift operator
Block diagram analysis, pole assignment and discrete-time PI control
System Identification

## Slide 25: Timetable
1
2
Concept of Feedback, Terminology and Objectives of Control
Transfer Functions represented using the
Backward Shift operator
3
System
Identification
pole assignment and 4
Block diagram analysis,
discrete-time PI control
5
Introduction to “Modern Control”
Theory
State variable
feedback using non-minimal state space models
CORE TOPIC
6
Optimal control
Multivariable & Non-linear
Robust control
Feed-forward control
Stochastic control

## Slide 26: Short Exercise…
Are the objectives clear?
What do you hope to learn from this module?
What do you expect to be the most challenging part?

## Slide 27
ENGR506
1.3 Feedback

## Slide 28: Case Study
A common actuator is a DC motor which provides direct rotary motion or, via drums and cables, translational motion
For the purposes of this example, there is an applied Input voltage U and a shaft speed Output X
This U and X notation is used throughout the module (either X or Y is used for the output)
https://en.wikipedia.org/wiki/DC_motor#
/media/File:Electric_motor_cycle_2.png

## Slide 29: Step Response
motor speed
input signal
Plant
X
U
Actual Motor Speed (Volts)
Input Signal
(Volts)

## Slide 30: Open–Loop Control
D
Desired Motor Speed (Volts)
Plant
X
U
Actual Motor Speed (Volts)
Input Signal (Volts)
Controller

## Slide 31
U  Kp  D
(Control Algorithm)
Select control algorithm (here, Proportional)
Optimise or “tune” algorithm (here, numerical value of Kp)
Proportional Control (Open–Loop form)
Plant
X
U
Actual Motor Speed (Volts)
Input Signal (Volts)
Desired Motor Speed (Volts)
D
Controller
K p

## Slide 32
Open–Loop Control of a DC Motor (Zero Disturbances)
200
400
600
800
22
20
18
200
400
600
800
1
0.5
0
200
400
600
samples
800
0.05
0
-0.05
Output
Control Input
Disturbance (zero)
Kp?
Notes: What is Value of Kp?

## Slide 33
Open–Loop Control of a DC Motor (Square Disturbances)
200
400
600
800
25
20
15
200
400
600
800
200
1
Control Input 0.5
0
400
sample
600
800
-0.05
0.05
0
Output
Disturbance

## Slide 34
Closed–Loop Control of a DC Motor (Feedback Loop)
Plant
X
U
Actual Motor Speed (Volts)
Input Signal (Volts)
K p
Controller
D

For a DC motor, output X is measured with a tachometer, usually a small permanent–magnet that returns a voltage proportional to shaft speed
Desired Motor Speed (Volts)

## Slide 35
Closed–Loop Control of a DC Motor (Disturbances)
200
400
600
800
22
20
18
200
400
600
800
1
0.5
0
200
400
600
samples
800
0.05
0
-0.05
Output
Control Input
Disturbance
(Results above are for “Integral” control: see later)

## Slide 36
Comparison of Open and Closed–Loop Control
200
400
sample
600
800
12
14
22
20
18
16
26
24
Closed–loop
Open–loop

## Slide 37: Advantages of Feedback
Improved transient response
Decreased sensitivity to modelling errors
Decreased sensitivity to disturbances
Ability to eliminate steady state errors
(with inclusion of suitable control elements)
Stabilisation of an unstable system

## Slide 38
Closed–Loop Control of a DC Motor (Analysis & Design)
Plant
X
U
Actual Motor Speed (Volts)
Input Signal
(Volts)
K p
Controller

Desired Motor Speed (Volts)
D
G
Mathematical analysis using a model to help optimise the control design

## Slide 39: Closed–Loop Control of a DC
Motor (Implementation)
Plant
X
U
Actual Motor Speed (Volts)
Input Signal (Volts)
K p
Controller

Desired Motor Speed (Volts)
D
Implementation of the optimised
control algorithm on the real system

## Slide 40: Closed–Loop Control
(Key Terminology)
Control input(s)
Controller System
X or Y
Output(s)
minimise the difference between the measured output and the desired output (plus other control objectives)
Desired output
response
U
D
r
yd
System, also commonly called the plant or the process
Desired output response, also called the set point, the command input or the reference level
Controller attempts to adjust the control input to

## Slide 41: Short Exercise…
Would you describe the control system for a kitchen toaster as open or closed–loop?
Solution – in a moment (audio)
https://en.wikipedia.org/wiki/Toaster#/media/File:Con sumer_Reports_-_Hamilton_Beach_Digital_toaster.tiff
More Examples?

## Slide 42: Open Loop Control Systems
Washing Machine
Electric Bulb
Electric Hand Drier
Time based Bread Toaster
Automatic Water Faucet
TV Remote Control
Electric Clothes Drier
Shades or Blinds on a window
Stepper Motor or Servo Motor
Inkjet Printers
Door Lock System
Traffic Control System

## Slide 43
CNENGR506
1.4 Control Objectives

## Slide 44
Closed–Loop Control (Recap)
Control input(s)
Controller
System
X or Y
Output(s)
Desired output
response
U
D
r
yd

## Slide 45
Proportional Control (Feedback Form)
yd
Y
U

## Slide 46: Integral Control (Smooth)
yd
Y
U

## Slide 47: Integral Control (Oscillatory)
yd
Y
U

## Slide 48: Four Standard Objectives
The closed–loop system should be stable
The output should track the desired output response in the steady state i.e. there should be no steady state error
The transient behaviour of the system should be
satisfactory
The control
system should reject disturbances
U
Y
y
d

## Slide 49: Commercial Aircraft
What is “satisfactory” transient behaviour? What about … safety, operating costs, robustness, etc. And who decides the set point?
https://en.wikipedia.org/wiki/Military_aircraft#/media/F ile:Aermacchi_T-346A_5D4_1066_(43074148234).jpg
More Examples in Tutorial

## Slide 50: Assignment-Homework
Choose any one area (some are given below) and provide an example to Appy Four objectives of the Closed Loop Control systems.
Industrial Manufacturing
Robotics
Agriculture
Aerospace
Traffic Management
Telecommunications etc……

## Slide 51: Conclusions
Introduction
Syllabus
Feedback
Control Objectives