## Slide 1
CNENGR506
Intelligent System Control

## Slide 2: Syllabus
1
2
Concept of Feedback, Terminology and Objectives of Control
Transfer Functions represented using the
Backward Shift operator
3
System
Identification
pole assignment and 4
Block diagram analysis,
discrete-time PI control
5
Introduction to “Modern Control”
Theory
State variable
feedback using non-minimal state space models
CORE TOPIC
6
Optimal control
Multivariable & Non-linear
Robust control
Feed-forward control
Stochastic control

## Slide 3: ENGR406 (506) Intelligent System Control
Contents
Part 1 – Terminology and Objectives of Control
Part 2 – Discrete–Time Transfer Function Models
Part 3 – System Identification
Part 4 – Discrete–Time Control & Pole Assignment
Part 5 – State Variable Feedback
Part 6 – Additional Topics & Case Studies

## Slide 4
Part 2 – Discrete–Time Transfer Function Models
Contents
Section 2.1 – Why Model?
Section 2.2 – Types of Model
Section 2.3 – Difference Equations
Section 2.4 – Backward Shift Operator
Section 2.5 – Steady state Gain
Section 2.6 – Poles and Stability
Section 2.7 – Block Diagrams

## Slide 5: Cause and Effect
system
inputs
outputs

## Slide 6: Single-Input, Single-Output
system
input
output

## Slide 7: Illustrative Model
1
2
3
b1z  b2 z
b3 z
1 2
3
1 a1z  a2 z  a3 z
yk
uk
discrete-time Transfer Function
(backward shift operator,
some people use z, q, B, etc.)
input
output

## Slide 8: Numerical Example
27.4671z1  65.6418z2  91.1006z3
1 2.4425z1  2.2794z2  0.8274z3
k
y
k
u
discrete-time Transfer Function
input
output

## Slide 9
What is a Mathematical Model?
A scientific hypothesis about the behaviour of the system under study
Mathematical modelling is the process of describing a real world problem in mathematical terms, usually in the form of equations,
Why model?
  Scientific understanding
  Forecasting
  Simulation
  Management & Operational Planning
  Optimisation
  Control system design
Notes: Mathematical modelling is the process of describing a real world problem in mathematical terms, usually in the form of equations,

## Slide 10: The Scientific Method
10
Karl Popper (1959) … Scientific proof proceeds via
repeated exercises aimed at falsification

## Slide 11
Modelling Flow Chart
Definition of Obje ctives
A priori data and information
Mode l structure formulation
Speculative Bayesian
simulation modelling
Mode l structure ide ntification
Relevant data
colle ction
Parame ter estimation
Mode l falsification
exercises
Additional data
colle ction
Mode l conditionally
Mode l usable
the model: simulation, forecasting, operational control, management,
planning, optimisation
valid
Yes
Mode l acce ptable
Yes
Analyse nature of limitations
S ystems analysis and synthesis using
main iterative loop
Planning stage
No
No
Yes
No
11

## Slide 12
Modelling Tree Diagram (1)
Linear model
Nonlinear model
Lumped or distributed parameter model
Mechanistic model
Black box model
Continuous- time model
Discrete- time model
Deterministic
Stochastic
Grey box model

## Slide 13: Ventilation Chamber

## Slide 14: Main Airflow Patterns
Clockwise Rotation 250-300 m3/h
Anti-clockwise Rotation 80-220 m3/h
Intermediate Flow
~240 m3/h

## Slide 15
Computational Fluid Dynamics (PHOENICS)

## Slide 16
Modelling Tree Diagram (2)
Linear model
Nonlinear model
Lumped or distributed parameter model
Mechanistic model
Black box model
Continuous- time model
Discrete- time model
Deterministic
Stochastic
Grey box model

## Slide 17: Ventilation Rate Control for Different Operating Points
0
10
20
30
40 50 60
percent
70
80
90
100
0
1000
2000
3000
4000
5000
6000
Ventilation Rate vs. Voltage
m3/h
0 50 100 150 200 250
0
2000
4000
6000
0 50 100
150 200 250
Time (s)
0
20
40
60
80
100
Ventilation rate and set point
Control input

## Slide 18
Modelling Tree Diagram (3)
Linear model
Nonlinear model
Lumped or distributed parameter model
Mechanistic model
Black box model
Continuous- time model
Discrete- time model
Deterministic
Stochastic
Grey box model

## Slide 19
Modelling Tree Diagram (3)
Linear model
Nonlinear model
Lumped or distributed parameter model
Mechanistic model
Black box model
Continuous- time model
Discrete- time model
Deterministic
Stochastic
Grey box model

## Slide 20
Glasshouse Actuators for Humidity, Temperature and Carbon Dioxide
CO2 supply pipe
Heating pipe

## Slide 21
Glasshouse Model using Simulink

## Slide 22: Open–Loop Experiment
Measured Data from a Venlo Glasshouse, Bedford, UK

## Slide 23
Control Model for Temperature
0.65z2
y(k )  u(k )
1 0.91z1

## Slide 24: Mechanistic Models
Model represents the scientists prior perception of the system, based on an interpretation of ‘known’ physical laws. Prejudicial?
Characterised by parameters that have direct physical meaning, such as mass or electrical resistance
Data may be used to ‘validate’ the model
Simple mechanistic models can be used for control system design but these models are arguably more appropriate for simulation purposes

## Slide 25: Data–Based Models
Obtained by direct reference to data.
These data are used to identify both the model structure and estimate the parameters using statistical analysis
The model is usually a black box relating the input and output variables in the simplest possible manner
Dominant mode model, ideal for control system design

## Slide 26
Data–Based
Mechanistic (DBM) Models
Data are used to both identify the model structure and estimate the parameters using statistical analysis
But the DBM model only credible if it also is capable of interpretation in a physically meaningful manner
Contrasts with mechanistic models e.g. CFD
Also differs from ‘grey-box’ modelling

## Slide 27: Derwent River Model
Nonlinear Element
Dynamic Model
Rainfall
Effective Rainfall
River Flow
https://commons.wikimed ia.org/wiki/File:Generic_U K_flood_image.jpg
http://www.nnvl.noaa.gov/view/#GOES

## Slide 28: Dynamic Model
Obtained by statistical estimation from the hourly measured flow and effective rainfall
y(t) is the river flow output
u(t) is the “effective rainfall” input
s is the differential operator, i.e. d/dt
0.01706s2  0.1578s  0.001680
s2  0.3299s  0.001768
y(t) 
u(t)

## Slide 29: Exercise
Linear model
Nonlinear model
Lumped or distributed parameter model
Mechanistic model
Black box model
Continuous- time model
Discrete- time model
Categorise the model on the previous slide (i.e. for the relationship between effective
rainfall and river flow)
Solution – in a moment

## Slide 30: DBM Example
0.1496
0.002573 u(t)
y(t)  0.0171
s  0.3244 s  0.00545 

Applying partial fraction expansion, the river flow model can be written in parallel pathway form as above. This has the following practical interpretation:
  An instantaneous effect accounting for the small amount of effective rainfall that affects the river flow within 1 hour
  A ‘quick–flow’ effect with steady state gain and residence time or time constant (see later lecture) that is associated with surface and near surface processes
  A ‘slow–flow’ effect with steady state gain and residence associated with groundwater processes

## Slide 31
Modelling Tree Diagram (4)
Linear model
Nonlinear model
Grey box model
Lumped or distributed parameter model
Mechanistic model
Black box model
Continuous- time model
Discrete- time model
Deterministic
Stochastic
Also: analytical solution vs. numerical solution; steady state vs. fully dynamic or Monte Carlo, etc.
0.65z2
1 0.91z1
y(k ) 
u(k )

## Slide 32
Part 2 – Discrete–Time Transfer Function Models
Contents
Section 2.1 – Why Model?
Section 2.2 – Types of Model
Section 2.3 – Difference Equations
Section 2.4 – Backward Shift Operator
Section 2.5 – Steady State Gain
Section 2.6 – Poles and Stability
Section 2.7 – Block Diagrams

## Slide 33
Basic Notation
y
y(t)
y(0), y(t), y(2t)  y(Nt)
y(k ) y(k 1)
yk yk 1
y(k 1)
yk 1

## Slide 34
Model for Vehicle Speed
We will develop a continuous-time, linear, mechanistic model for vehicle displacement and speed
Only for context and comparison with the discrete models used in this module!
y
y
y

## Slide 35
Free Body Diagram
m
velocity
displacement
acceleration
y
y
y
u(t)
by
u(t)  dy  my my  dy  u(t) mx  dx  u(t)
x is the velocity

## Slide 36
First Order, Continuous–Time
Differential Equation
m x  x  1 u(t)
d d
See e.g. the analytical solution in response to a unit step input
x(t)  1 1 ed t m 
d
time
Output
Input

## Slide 37: Reservoir Model
We will develop a discrete-time, linear, mechanistic model of a reservoir
Net inflow u(k)
Depth of water y(k)
https://en.wikipedia.org/wiki/Reservoir#/ media/File:Lakevyrnwysummer.jpg

## Slide 38
Reservoir Model Mechanistic Development
V (k )  V (k  1)  I (k  1)  O(k  1)  V (k  1)
V (k )  A  y(k )
u(k )  I (k )  O(k )
Ay(k )  Ay(k 1)  u(k 1)   Ay(k 1)
y(k )  ay(k  1)  bu(k  1)
Exercise: show that b  1 A, a   1

## Slide 39: First Order, Discrete-Time Difference Equation
In this module, this is important notation
y(k )  ay(k  1)  bu(k  1)
Later, we will introduce more than just two parameters, hence could use subscripts
y(k )  a1 y(k 1)  b1u(k 1)

## Slide 40
Reservoir Model Step Response (1)
Output
Input
u(k  2)  1 otherwise zero
u(0)  0, u(1)  0, u(2)  0, u(3)  1, u(4)  1, 
b  0.2
a  0.8
y(0)  0
y(k)  0.8 y(k 1)  0.2u(k 1)
y(1)  0
y(2)  0

## Slide 41: Reservoir Model
Step Response (2)
y(k)  0.8 y(k 1)  0.2u(k 1)
u(2)  0, u(3)  1, u(4)  1,
y(0)  y(1)  y(2)  0
y(3)  0.80  0.2 0  0
y(4)  0.80  0.2 1  0.2 y(5)  0.80.2  0.2 1  0.36
y(6)  0.80.36  0.2 1  0.49
y(7)  0.80.49  0.2 1  0.59

## Slide 42: Reservoir Model Step Response (Table)
y(3)  0.80  0.2 0  0 y(4)  0.80  0.2 1  0.2 y(5)  0.80.2  0.2 1  0.36
y(6)  0.80.36  0.2 1  0.49
y(7)  0.80.49  0.2 1  0.59
k | u(k ) | u(k 1) | y(k)
2 | 0 | 0 | 0
3 | 1 | 0 | 0
4 | 1 | 1 | 0.2
5 | 1 | 1 | 0.36
6 | 1 | 1 | 0.49
7 | 1 | 1 | 0.59

## Slide 43
Laboratory Axial Fan in Ventilation Chamber
A discrete-time, linear, data-based model will be presented
Parameter values have already been estimated by the lecturer (from data)
Hence, this example is again about how to use the model e.g. to examine the step response

## Slide 44: Axial Fan Block Diagram
y(k )
airflow
u(k )
voltage

## Slide 45
Open–Loop Experimental Data (and Model Response)

## Slide 46: Axial Fan Model
y(k )
u(k )
voltage
airflow
y(k)  a1 y(k 1)  b1u(k 1)
y(k)  0.8 y(k 1) 1.6u(k 1)

## Slide 47
Step Response of the Axial Fan Model
y(k)  0.8 y(k 1) 1.6u(k 1)
k u(k ) u(k 1) y(k)
4 0 0
0
5
1 0
0
6
1
1
1.6
7
1
1
2.88
8
1
1
3.90
9
1
1
4.72
y(k)  0.8(0) 1.6(1)  1.6
y(k)  0.8(1.6) 1.6(1)  2.88
y(k)  0.8(2.88) 1.6(1)  3.90
0
10
20
30
40
50
0
2
4
6
sample no.
output
control input

## Slide 48
Response using the Experimental Data
Compare model with data i.e. simulate from initial conditions as above
Becomes tedious to solve by hand!
Use MATLAB function filter
Or can use SIMULINK filter

## Slide 49
Part 2 – Discrete–Time Transfer Function Models
Contents
Section 2.1 – Why Model?
Section 2.2 – Types of Model
Section 2.3 – Difference Equations
Section 2.4 – Backward Shift Operator
Section 2.5 – Steady State Gain
Section 2.6 – Poles and Stability
Section 2.7 – Block Diagrams

## Slide 50: Backward Shift Operator
z1
k 1
y
k
y
1
yk  yk 1
z
2
yk  yk 2
z

## Slide 51
Discrete-Time Transfer Function (First Order Example)
yk  a1 yk 1  b1uk 1
yk  a1 yk 1  b1uk 1
Difference Equation
yk  a1z1 yk  b1z1uk
1 a1z1  yk  b1z1uk
Transfer Function
b z1
1
1
1 a1z
yk 
uk

## Slide 52
Discrete-Time Transfer Function (Block Diagram)
1
b1z
1
1 a1z
yk
uk
1
b1z
1
1 a1z
k
k
y 
u

## Slide 53
Discrete-Time Transfer Function (Reservoir Model)
0.2z1
1 0.8z1
yk
uk

## Slide 54
Discrete-Time Transfer Function (Axial Fan Model)
1.6z1
1 0.8z1
yk
uk

## Slide 55
Discrete-Time Transfer Function (Reverse)
1
b1z
1
1 a1z
k
k
y 
u
Transfer Function
1 a1z1  yk  b1z1uk
yk  a1z1 yk  b1z1uk
Difference Equation
yk  a1 yk 1  b1uk 1

## Slide 56: Model for a Wind Turbine
https://en.wikipedia.org/wiki/Wind_turbine#/media/File:Turbin e_Blade_Convoy_Passing_through_Edenfield.jpg
https://en.wikipedia.org/wiki/Wind_turbine#/ media/File:Windmills_D1- D4_(Thornton_Bank).jpg

## Slide 57: Open-Loop Simulation Data
Poorly damped
Generator reaction torque y(k)
Pitch angle u(k)
Aim to keep the turbine components within designed speed and torque limits
0
20
40
60
80
100
0
200
600
400
output
0
20
40
60
80
100
0
0.5
1
input
sample no.
yk
k
u

## Slide 58: Third Order Model
1
2
b0  b1z
b2 z
1
2
3
1 a1z
a2 z
a3 z
yk  a1 yk 1  a2 yk 2  a3 yk 3  b0uk  b1uk 1  b2uk 2
yk  a1z1 yk  a2 z2 yk  a3 z3 yk  b0uk  b1z1uk  b2 z2uk
1 a1z1  a2 z2  a3 z3  yk  b0  b1z1  b2 z2 uk
yk
uk

## Slide 59: Time Delays
0
5
10
15
0
200
600
400
0
5
10
15
0
0.5
1
1.5
yk
uk
https://en.wikipedia.org/wiki/Wind_turbine#/ media/File:Windmills_D1- D4_(Thornton_Bank).jpg

## Slide 60
Wind Turbine with Time Delay
yk  a1 yk 1  a2 yk 2  a3 yk 3  b3uk 3  b4uk 4  b5uk 5
yk  a1z1 yk  a2 z2 yk  a3 z3 yk  b3 z3uk  b4 z4uk  b5 z5uk
b0 = b1 = b2 = 0
3
4
5
b3 z  b4 z
b5 z
1
2
3
1 a1z
a2 z
a3 z
yk
uk
time delay

## Slide 61
Generalised Discrete-Time Transfer Function Model
1
1
b0  b1z
1
2
1
1 a1z
a2 z
 B( z ) u
A(z )
m
 bm z
k
k
k
n
 anz
y 
u
B(z1)
A(z1)
yk
Minimal state space models have n states – see later
uk
n is the order of the system

## Slide 62: Unity Time Delay Version
1
1
b1z  bm z
1
2
1
1 a1z
a2 z
 B( z ) u
A(z )
m
k
k
k
n
 anz
y 
u
B(z1)
A(z1)
The model we will use later for control system
design has at least 1 sample time delay, hence b0 = 0
yk
uk

## Slide 63
Part 2 – Discrete–Time Transfer Function Models
Contents
Section 2.1 – Why Model?
Section 2.2 – Types of Model
Section 2.3 – Difference Equations
Section 2.4 – Backward Shift Operator
Section 2.5 – Steady State Gain
Section 2.6 – Poles and Stability
Section 2.7 – Block Diagrams

## Slide 64: Steady State Gain
y(k )  y(k 1)  0
y(k )(1 z1 )  0
z1  1
The gain tells us the magnitude of the output relative to the input at steady state
To find the steady state gain of a discrete-time Transfer Function, set the backward shift operator to unity
To find the steady state value of the output, multiply the gain by the value of the input

## Slide 65
Steady State Gain (General Transfer Function Model)
b1  b2  bm
0
0
 1 a1  a2  an 

y(k  ) 

u  G u
 
This slide shows the steady state gain of the generalised Transfer Function model i.e. G
It also shows that the output asymptotically approaches a value of G multiplied by u0, where u0 is a constant input (in the case of a unit step response, u0 = 1)

## Slide 66: Steady State Gain (Axial Fan)
1.6z1
1 0.8z1
yk
uk
8
0
u
y(k  )

## Slide 67: Step Response (Axial Fan)
0
10
20
30
40
50
0
2
8
6
output
4
sample no.
control input

## Slide 68
Steady State Gain (Reservoir Model)
0.2z1
1 0.8z1
yk
uk
1
0
u
y(k  )

## Slide 69: Wind Turbine Model
27.4671z1  65.6418z2  91.1006z3
1 2.4425z1  2.2794z2  0.8274z3
k
y
k
u
discrete-time Transfer Function
input
output

## Slide 70
Backward Shift Operator Set to Unity
27.4671 65.6418  91.1006
1 2.4425  2.2794  0.8274
y(k  )
u0
steady state gain
input
output

## Slide 71
Steady State Gain for the Wind Turbine Model
211.4
y(k  )
u0
steady state gain
input
output

## Slide 72
Step Response (Wind Turbine)
0
20
40
60
80
100
output
600
400
200
0
0
20
40
60
80
100
input
1
0.5
0
sample no.

## Slide 73: Time Constant
The continuous–time concept of a time constant is referred to occasionally in this module.
It relates to the analytical solution for the unit step response of a first order differential equation
It is the time taken for the output to reach 63% of the steady state value

## Slide 74: Time Constant for Reservoir Model
1
b1z
1
1 a1z
k
k
y 
u
loge (a1 )
t
T  
e.g. Reservoir model with 1 hour sampling rate
0.2z1
yk  1 uk
1 0.8z
T    4.5 hours
log (0.8)
1
e

## Slide 75
Unit Step Response for Reservoir Model
For this model, there is a one sample time delay and the steady state gain is 1.0
The output reaches 0.63 m (water depth) 4.5 hours after the “start” of the step response
Can be used to represent the speed of response
4.5 hours

## Slide 76
Part 2 – Discrete–Time Transfer Function Models
Contents
Section 2.1 – Why Model?
Section 2.2 – Types of Model
Section 2.3 – Difference Equations
Section 2.4 – Backward Shift Operator
Section 2.5 – Steady state Gain
Section 2.6 – Poles and Stability
Section 2.7 – Block Diagrams

## Slide 77: Stable System
0
5
10 15
Time (seconds)
20
25
-100
0
100
200
300
400
500
600
Generator Reaction Torque
“If a system that is initially in equilibrium is disturbed, it is said to be stable if it eventually returns to an equilibrium condition”

## Slide 78: Unstable System
3
4
5
6
7
8
9
10
Time
0
0.5
1
1.5
2
2.5
Output
10 4

## Slide 79
Step Response of the Axial Fan Model
y(k)  0.8 y(k 1) 1.6u(k 1)
stability
y(k)  0.8 y(k 1)
0
10
20
30
40
50
0
2
4
6
8
sample no.
output
control input
k | u(k ) | u(k 1) | y(k) |  | 
4 | 0 | 0 | 0 |  | 
5 | 1 | 0 | 0 |  | 
6 | 1 | 1 | 1.6 |  | 
7 | 1 | 1 | 2.88 |  | 
8 | 1 | 1 | 3.90 |  | 
9 | 1 | 1 | 4.72 |  | 

## Slide 80
Stability of the First Order Model
y(k)  0.8 y(k 1) 1.6u(k 1)
1.6z1
y(k )  u(k ) 1 0.8z1
1
1
1
y(k)  a y(k 1)  b u(k 1)
b1z
1
1 a1z
y(k) 
u(k )
From the previous slide, we see that, for stability, negative a1 (which takes the value 0.8 for the fan model) should be less than 1.0. Negative a1 is called the pole.

## Slide 81
Backward and Forward Shift Operators
z1 y(k )  y(k 1)
zy(k )  y(k 1)
Standard rules of algebra apply!
z1  1
z
z1z  1
z5 z2  z3
Etc.

## Slide 82: Fan Model Pole and Stability
1.6z1
y(k )  u(k ) 1 0.8z1
TF model
1 0.8z1
TF denominator – characteristic polynomial
1 0.8z1  0
Characteristic equation
z  0.8  0
Convert to z domain
z  0.8
Pole, less than 1.0, hence the model is “Stable”

## Slide 83: Poles and Stability
1
2
1 a1z
a2 z
 anz  0
n
zn  a1zn1  a2 zn2  an  0
Solve for z – the roots of this equation are called the poles pi and for stability:
pi
 1
i  1, 2, , n

## Slide 84: Comments
exponential (stable or unstable)
Roots of the characteristic equation are called the poles
We use the forward shift (not backward shift) to examine the stability, so that poles inside the unit circle imply stability
Poles might be real or complex conjugate pairs, or a mixture of both
Complex poles imply the system might oscillate
If there are no complex poles, the response will be

## Slide 85: Wind Turbine Model
0.9212
1 2.4425z1  2.2794z2  0.8274z3  0
z3  2.4425z2  2.2794z  0.8274=0
>> roots([1 -2.4425, 2.2794, -0.8274])
ans =
0.9751
0.7337 + 0.5570i
0.7337 - 0.5570i
>> abs(ans) ans =
0.9751
0.9212

## Slide 86
General Discrete-Time Transfer Function Model
1
1
b0  b1z
1
2
1
1 a1z
a2 z
 B( z ) u
A(z )
m
 bm z
k
k
k
n
 anz
y 
u
B(z1)
A(z1)
yk
uk

## Slide 87: Illustrative Model Responses
0
10
20
30
40
50
10 20 30
marginally stable system
40
50
0.4
0.2
0
-0.2
stable, non-minimum phase system
0
10
5
0
sample no.
0.4 | stable system |  |  | 
0.2 |  |  |  | 
0 |  |  |  | 
0 | 10 20 | 30 | 40 | 50

## Slide 88
Part 2 – Discrete–Time Transfer Function Models
Contents
Section 2.1 – Why Model?
Section 2.2 – Types of Model
Section 2.3 – Difference Equations
Section 2.4 – Backward Shift Operator
Section 2.5 – Steady state Gain
Section 2.6 – Poles and Stability
Section 2.7 – Block Diagrams

## Slide 89: Block Diagram Analysis
Earlier videos concerned the analysis of a single Transfer Function in isolation
In control system design scenarios, we may have several linked Transfer Functions representing, for example, the model and the control algorithm
Block diagram analysis is a straightforward way of combining several Transfer Functions into one “overall”
Transfer Function, ready for further analysis
(e.g. stability of a control system)

## Slide 90
Single Transfer Function (or Scalar Gain)
x2 (k )
G1
x1(k )
x2 (k)  G1x1(k)

## Slide 91: Series Rule
G2
x3 (k )
x2 (k )
G1
x1(k )
x3 (k )  G2 x2 (k )  G2 G1  x1(k )  G2G1x1(k )  G1G2 x1(k )
x1(k )
x3 (k )
G1G2

## Slide 92
Series Rule showing Numerator and Denominator
B(z1)
A(z1)
x3 (k )
x2 (k)
C(z1)
D(z1)
x1(k )
C(z1)B(z1)
D(z1) A(z1)
x3 (k )
x1(k )

## Slide 93: Negative Feedback Rule
G1

x1(k ) 
G2
x2 (k)
x2 (k)  G1  x1(k)  G2 x2 (k )
G1
2
1
1 2
x (k ) 
x (k )
1 G G

## Slide 94
Negative Feedback Rule Example (Original Diagram)
B(z1)
A(z1)
r(k ) 

C(z1)
D(z1)
y(k )

## Slide 95
Negative Feedback Rule Example (Reduced Form)
 B(z1) 
1
 C(z1)  B(z1) 
1
1
A(z )
1
D(z )
A(z )




 

 







y(k )
r(k )
B(z1)D(z1)
D(z1) A(z1)  C(z1)B(z1)
y(k )
r(k )

## Slide 96
Footnote –
High Gain Control
G
r


y
k
1 k G
k G
y  r
Consider what if k G >> 1
then y = r

## Slide 97: Conclusions
This section has considered:
– Why Model?
– Types of Model
– Difference Equations
– Backward Shift Operator
– Steady state Gain
– Poles and Stability
– Block Diagrams