## Slide 1
CNENGR506
Intelligent System Control

## Slide 2: Syllabus
1
2
Concept of Feedback, Terminology and Objectives of Control
Transfer Functions represented using the
Backward Shift operator
3
System
Identification
pole assignment and 4
Block diagram analysis,
discrete-time PI control
5
Introduction to “Modern Control”
Theory
State variable
feedback using non-minimal state space models
CORE TOPIC
6
Optimal control
Multivariable & Non-linear
Robust control
Feed-forward control
Stochastic control

## Slide 3: ENGR406 (506) Intelligent System Control
Contents
Part 1 – Terminology and Objectives of Control
Part 2 – Discrete–Time Transfer Function Models
Part 3 – System Identification
Part 4 – Discrete–Time Control & Pole Assignment
Part 5 – State Variable Feedback
Part 6 – Additional Topics & Case Studies

## Slide 4
Part 4 – Discrete–Time Control & Pole Assignment
Contents
Section 4.1 – Proportional Action
Section 4.2 – Integral Action
Section 4.3 – Motorway Traffic
Section 4.4 – Pole Assignment

## Slide 5: Design Process
Control model used to directly estimate the parameters (or gains) of the controller
Simulation model
(if available) used to evaluate the controller before implementation
Identification of data-based model
Estimation of control algorithm
Evaluation by simulation
Implementation

## Slide 6: Example – Axial Fan
y(k )
airflow
u(k )
voltage

## Slide 7: Example – Axial Fan Model
y(k )
u(k )
voltage
airflow
1.6z1
1 0.8z1

## Slide 8: Proportional Control
Set point, i.e. desired -
ventilation rate
+
yd (k) kp
u(k )
y(k)
bz1
1  az1
Control Algorithm:
u(k )  kp  yd (k )  y(k )

## Slide 9
Block Diagram Analysis – Series Rule
G2
y(k )
G1
e(k )
e(k )
y(k )
G1G2

## Slide 10
Block Diagram Analysis – Unity Negative Feedback
G1

r(k ) 
1
y(k )
G1
1 G1
y(k ) 
r(k )

## Slide 11
Closed Loop Transfer Function
u(k )
y(k)
+
-
bz1
1  az1
yd (k) kp
 
k bz1
1
y (k )
1 a  k b z
p
d
p
bz1
1
bz1
1
1 az
y(k ) 
y (k ) 
1 k
1 az
p 

d
p 

k








Poles of the plant: –a Control system: –a – kpb
11

## Slide 12: Steady State Gain
u(k )
y(k)
+
-
bz1
1  az1
yd (k) kp
y(k  ) 
1 a  k b
kpb
d
p
y
No steady state tracking

## Slide 13: Closed Loop Response
0
5
10
sample no.
15
20
0
0.2
command
1
0.8
output
0.6
0.4
control input

## Slide 14: Hydraulic Manipulators
a1  1

## Slide 15
Part 4 – Discrete–Time Control & Pole Assignment
Contents
Section 4.1 – Proportional Action
Section 4.2 – Integral Action
Section 4.3 – Motorway Traffic
Section 4.4 – Pole Assignment

## Slide 16: Example – Axial Fan
y(k )
u(k )
voltage
airflow
1.6z1
1 0.8z1

## Slide 17
Integral Control
y(k )
+
-
1
bz1
1  az
yd (k )
Control system block diagram:
Control algorithm in difference equation form:
u(k )  u(k 1)  kI  yd (k )  y(k )
1
 
u(k )  z u(k )  k
y (k )  y(k )
I d
 


1
1 z u(k )  k
y (k )  y(k )
I
d
Control algorithm in TF form:
1  yd (k )  y(k )
u(k ) 
1 z
kI
kI 1  z1 | u(k)

## Slide 18
Transfer Function form to Difference Equation
 


1
1 z u(k )  k
y (k )  y(k )
I d
u(k )  u(k 1)  kI  yd (k )  y(k )
Control algorithm in difference equation form
 
1
u(k )  z u(k )  k
y (k )  y(k )
I d
y(k )
+
-
1
bz1
1  az
yd (k )
1  yd (k )  y(k )
u(k ) 
1 z
kI
Control algorithm in TF form
kI 1  z1 | u(k)

## Slide 19
Integral Control Sums the Error Signal
u(k )  u(k 1)  kI  yd (k )  y(k )
u(k 1)  u(k  2)  kI  yd (k 1)  y(k 1)
u(k  2)  u(k  3)  kI  yd (k  2)  y(k  2)
u(k 1)  u(k  3)  kI  yd (k  2)  y(k  2)  kI  yd (k 1)  y(k 1)
u(k )  u(k  3)  kI  yd (k  2)  y(k  2)
 kI  yd (k 1)  y(k 1)  kI  yd (k )  y(k )

## Slide 20
In a moment, standard algebra applies…
Multiply brackets out in the usual way
Powers sum in the usual way
 
1 
1
1 z 1 a1 z
1 1 1 1
 1 a1 z  z  a1 z z
1 1
2
 1 a1 z  z  a1 z

## Slide 21
bz1
1
1
bz1
1
1
I
1 z
1 az
y(k ) 
y (k )
1
I
1 z
1 az
d
 k 
 k 














Integral Control Closed Loop Transfer Function
y(k )
+
-
1
bz1
1  az
yd (k )
 

k bz1
1
1
1
y (k )
1 z 1 az  k bz
I
d
I

y (k ) 
k bz1
1 az1  z1  az2  k bz1
y(k ) 
I
d
I


k bz1
1
2
y (k )
1 a 1 k b z  az
I
d
I
kI 1  z1 | u(k)

## Slide 22
Integral Control Steady State Gain
y(k )
+
-
1
bz1
1  az
yd (k )
 
k bz1
1
2
y (k )
1 k b  a 1 z  az
I
d
I
bz1
1
1
bz1
1
1
I
1 z
1 az
y(k ) 
y (k ) 
1
I
1 z
1 az
d
 k 
 k 














y(k  ) 
1 kIb  a 1 a
I
yd  yd
k b
11
kI 1  z1 | u(k)
Type 1 servomechanism behaviour (steady state tracking of set point)

## Slide 23
Integral Control Illustrative Time Response
0
5
10
sample no.
15
20
0
0.2
0.6
0.4
0.8
command
1
output
control input

## Slide 24
Part 4 – Discrete–Time Control & Pole Assignment
Contents
Section 4.1 – Proportional Action
Section 4.2 – Integral Action
Section 4.3 – Motorway Traffic
Section 4.4 – Pole Assignment

## Slide 25
Ramp Metering Control on Motorways

## Slide 26
Utrecht to Amsterdam A2 Motorway

## Slide 27
M3 Motorway near Southampton
0
20
40
60
80
100
120
140
0
20
40
60
80
100
120
Velocity (km/hour)
Flow (veh/min)

## Slide 28: ALINEA Ramp Metering Algorithm
Motorway access control uses traffic lights on the entrance ramps
Vehicles temporarily delayed at the lights to avoid flow breakdown on motorway main carriageway
The industry standard algorithm (ALINEA) was based on simple integral control

## Slide 29
Part 4 – Discrete–Time Control & Pole Assignment
Contents
Section 4.1 – Proportional Action
Section 4.2 – Integral Action
Section 4.3 – Motorway Traffic
Section 4.4 – Pole Assignment

## Slide 30
Proportional-Integral (PI) Control
1 yd (k )  y(k ) f0 y(k )
u(k ) 
1 z
kI

## Slide 31: Exercise 1
Prove these are equivalent forms of the same PI control algorithm
1 yd (k )  y(k ) f0 y(k )
u(k ) 
1 z
kI
u(k)  u(k 1)  kI  yd (k )  y(k )  f0  y(k )  y(k 1)

## Slide 32: Exercise 2
Use the rules of block diagram analysis (or otherwise) to show that the closed-loop Transfer Function is as follows
Hint: simplify the inner feedback loop first i.e. the model and the proportional gain
k b z1
I 1
1
2
1 ( f0b1  a1 1 kI b1)z  (a1  f0b1)z
y(k ) 
yd (k )

## Slide 33
Steady State Gain and Characteristic Equation
k b z1
I 1
1
2
1 ( f0b1  a1 1 kI b1)z
 (a1  f0b1)z
y(k) 
yd (k )
I 1
1 f0b1  a1 1 kI b1  a1  f0b1
y(k  ) 
yd  yd
k b
2
z  ( f0b1  a1 1 kI b1)z  (a1  f0b1)  0

## Slide 34: Example – Axial Fan
y(k )
u(k )
voltage
airflow
1.6z1
1 0.8z1
a1  0.8
b1  1.6

## Slide 35: Pole Assignment
Pole assignment is a method for determining the control gains
In this example, we will apply the method to estimate gains for the PI controller i.e. to determine the proportional and integral gains
First step, determine the closed-loop Transfer Function and write down the characteristic equation:
2
z  ( f0b1  a1 1 kI b1)z  (a1  f0b1)  0

## Slide 36: Example 1 – Deadbeat
2
z  ( f0b1  a1 1 kI b1)z  (a1  f0b1)  0
p1  p2  0
D(z)   z  0 z  0  z2  0
( f0b1  a1 1 kI b1)  0 ; (a1  f0b1)  0
f0   a1 b1 f0  0.5
kI  1 b1
kI  0.625
10

## Slide 37: Deadbeat Time Response
0
5
10
sample no.
15
20
0
0.2
0.4
0.6
0.8
command
1
output
control input
What are the disadvantages of deadbeat control?
1  yd (k )  y(k )  0.5 y(k )
0.625
u(k ) 
1 z

## Slide 38: Example 2 – Complex Poles
2
z  ( f0b1  a1 1 kI b1)z  (a1  f0b1)  0
p1,2  0.6  0.3 j
D(z)   z  0.6  0.3 j  z  0.6  0.3 j   z2 1.2z  0.45  0
( f0b1  a1 1 kI b1)  1.2 ; (a1  f0b1)  0.45
f0  0.2188 kI  0.1563
12

## Slide 39: Complex Poles Time Response
1  yd (k )  y(k )  0.2188 y(k )
0.1563
u(k ) 
1 z
This design method is called pole placement or pole assignment
0
5
10
sample no.
15
20
0
0.2
0.4
0.6
0.8
command
1
output
control input

## Slide 40: Laboratory Results

## Slide 41: Recap
For a first order open loop system, with 1 numerator parameter and 1 time delay …
We obtained a 2nd order closed loop characteristic equation and compared it with the 2nd order desired characteristic equation
Two equations, 2 unknown control gains (note that a1 and
b1 have already been estimated)
The closed loop system is said to be controllable
i.e. we can place the poles at arbitrary positions on the complex z-plane

## Slide 42: Time Delays
y(k )
u(k )
voltage
airflow
0.027z2
1 0.743z1
y(k )  0.743y(k 1)  0.027u(k  2)
0.027z2
y(k )  u(k )
1 0.743z1

## Slide 43
Third Order Closed Loop Transfer Function
y(k )
u(k )
voltage
airflow
0.027z2
1 0.743z1
11.743z1  0.743  0.027 f0  0.027kI  z2  0.027 f0 z3
0.027k z2
y(k ) 
yd (k )
I

## Slide 44: Higher Order Systems
yk
uk
pitch angle
torque
b z3  b z4  b z5
3 4 5
1
2
3
1 a1z  a2 z
a3 z
wind turbine

## Slide 45: Limitations of PI control
19
In the case of time delays and/or higher order systems, the order of the closed-loop transfer function is increased, but there are still only 2 control gains
We cannot assign the closed loop poles to arbitrary positions on the complex z-plane i.e. the closed loop system is uncontrollable
The solution is to introduce additional feedback terms,
i.e. more control gains
State variable feedback provides one approach to this