## Slide 1: introduction
Dr. Muhammad Abrar (Dr. MAB)
m.abrar@lancaster.ac.uk
CNSCC.405
Digital Signal Processing
CNSCC.405: Digital Signal Processing

## Slide 2: Wireless Communication
Transmitting voice and data using electromagnetic waves in open space (atmosphere)
Fig: https://www.frontiersin.org/articles/10.3389/fenrg.2022.889355/full
CNSCC.405: Digital Signal Processing

## Slide 3: Types of Wireless Communication
celullar
wireless computer network
radio service
CNSCC.405: Digital Signal Processing

## Slide 4: Why Wireless?
Freedom from wires
  No cost of installing wires or rewiring
  No bunches of wires running here and there
  Instantaneous communication without physical connection setup, e.g., Bluetooth and WiFi
Global Coverage
  Communications can reach where wiring is infeasible or costly, e.g., rural areas, old buildings, battlefields, vehicles and outer space (communication satellites)
Stay connected
  Roaming allows flexibility to stay connected anywhere and anytime
Flexibility
  Services reach you wherever you go
  Connect to multiple devices simultaneously
CNSCC.405: Digital Signal Processing

## Slide 5: Challenges
Network Challenges
    Scarce spectrum
    Demanding/diverse applications
    Reliability
    Ubiquitous coverage
    Seamless indoor/outdoor operation
Device Challenges
    Size, Power, Cost
    Multiple Antennas
    Multi-radio Integration
    Co-existence
    Fading
CNSCC.405: Digital Signal Processing

## Slide 6: Grand Challenges in Wireless Communications
Security, secrecy, and privacy
Resource and spectrum utilizations
Communication infrastructure
Energy efficiency enhancement
Integration of wireless information and power transfer
Wireless access techniques
Dynamic architecture and network functions analysis
Coding and modulation
Resource and interference management
https://www.frontiersin.org/articles/10.3389/frcmn.2020.00001/full
CNSCC.405: Digital Signal Processing

## Slide 7: Elements of wireless Communication
User
Source
Decoder
Channel
Decoder
Demod-
ulator
Estimate of
Message signal
Estimate of
channel code word
Received
Signal
Channel code word
Source
Source
Encoder
Channel
Encoder
Modulator
Message Signal
Modulated
Transmitted Signal
Wireless Channel
CNSCC.405: Digital Signal Processing

## Slide 8: Frequency Carries/Channels
The information from sender to receiver is carrier over a well-defined frequency band.
This is called a channel
Each channel has a fixed frequency bandwidth (in KHz) and Capacity (bit-rate)
Different frequency bands (channels) can be used to transmit information in parallel and independently.
CNSCC.405: Digital Signal Processing

## Slide 9: Wireless Channel
The mobile radio channels places fundamental limitations on the performance of wireless communication systems
The wireless transmission path may be
  Line of sight
  Non line of sight: obstructed by buildings, mountains, foliage etc.
Characteristics of the channel appear to change randomly with time, which makes it difficult to design reliable systems with guaranteed performance.
Modeling the radio channel have been one of the difficult parts of the mobile radio system design.
CNSCC.405: Digital Signal Processing

## Slide 10: Wireless Channel Impairments
Noise : Thermal noise (AWGN)
Path loss : The loss in power as the radio signal propagates.
Shadowing : Due to the presence of fixed obstacles in the radio path.
Fading : Combines the effect of multiple propagation path, rapid movement of mobile units and reflectors.
CNSCC.405: Digital Signal Processing

## Slide 11: Link budget
CNSCC.405: Digital Signal Processing
Link budget is an important tool in the design of radio communication systems.
Accounting for all the gains and losses through the wireless channel to the receiver, it allows for predicting the received signal strength along with the required power margin.
Path loss and fading are the two most important factors to consider in link budget.

## Slide 12: Link budget
CNSCC.405: Digital Signal Processing
The mean path loss is a deterministic factor that can be predicted with the distance between the transmitter and receiver.
Shadowing and small-scale fading are random phenomena, which means that their effects can only be predicted by their probabilistic distribution. For example, shadowing is typically modeled by a log-normal distribution.

## Slide 13: Radio Wave Propagation
CNSCC.405: Digital Signal Processing

## Slide 14: Radio Propagation Mechanisms
Reflection occurs when the electromagnetic wave impinges on an object which has very large dimensions as compared to the wavelength e.g., surface of the earth, buildings wall etc.
Diffraction occurs when the radio path between the transmitter and receiver is obstructed by a surface that has sharp irregularities (edges)
Scattering occurs when the medium has objects that are smaller or comparable to the wavelength (smaller objects, rough surfaces or other irregularities on the channel)
CNSCC.405: Digital Signal Processing

## Slide 15: What is Fading ?
Fading is a deviation or attenuation a signal experiences over a certain propagation media.
In wireless communication, fading may be due to multipath propagation or due to shadowing from obstacles.
CNSCC.405: Digital Signal Processing

## Slide 16: Classification of Fading Channels
CNSCC.405: Digital Signal Processing

## Slide 17: Large-scale fading vs. small-scale fading
CNSCC.405: Digital Signal Processing

## Slide 18: Large-Scale Fading
General Path Loss Model
CNSCC.405: Digital Signal Processing

## Slide 19
Free Space Propagation Model
The free space propagation model is used to predict received signal strength when the transmitter and receiver have a clear line-of-sight path between them.
  satellite communication
  microwave line-of-sight radio link
Friis free space equation
  : transmitted power : T-R separation distance (m)
  : received power : system loss
  : transmitter antenna gain : wavelength in meters
  : receiver antenna gain
CNSCC.405: Digital Signal Processing

## Slide 20
The gain of the antenna
: effective aperture is related to the physical size of the antenna
The wavelength is related to the carrier frequency by
: carrier frequency in Hertz
: carrier frequency in radians
: speed of light (meters/s)
The losses are usually due to transmission line attenuation, filter losses, and antenna losses in the communication system. A value of L=1 indicates no loss in the system hardware.
CNSCC.405: Digital Signal Processing

## Slide 21
  Isotropic radiator is an ideal antenna which radiates power with unit gain.
Effective isotropic radiated power (EIRP) is defined as
and represents the maximum radiated power available from transmitter in the direction of maximum antenna gain as compared to an isotropic radiator.
Path loss for the free space model with antenna gains
When antenna gains are excluded
The Friis free space model is only a valid predictor for for values of d which is in the far-field (Fraunhofer region) of the transmission antenna.
CNSCC.405: Digital Signal Processing

## Slide 22
  The far-field region of a transmitting antenna is defined as the region beyond the far-field distance
where D is the largest physical linear dimension of the antenna.
To be in the far-filed region the following equations must be satisfied and
Furthermore, the following equation does not hold for d=0.
Use close-in distance and a known received power at that point
or
CNSCC.405: Digital Signal Processing

## Slide 23
The Friis equation can be modified to accommodate different environments, on the reason that the received signal decreases as the nth power of distance, where the parameter n is the path-loss exponent (PLE) that takes constant values depending on the environment that is modeled (see Table below} for various empirical values for PLE).
CNSCC.405: Digital Signal Processing

## Slide 24
free-space path loss at the carrier frequency of fc = 1.5 GHz for different antenna gains as the distance varies.
Free-space Path Loss Model.
CNSCC.405: Digital Signal Processing

## Slide 25
1. Suppose a transmitter produces 50W of power. a. Express the transmit power in units of dBm and dBW.
    b. If the transmitter’s power is applied to a unity gain antenna with a 900-MHz carrier frequency, what is the received power in dBm at a free space distance of 100 m?
    c. Repeat (ii) for a distance of 10km.
    d. Repeat (ii) (iii) under ground reflected model with the height of the transmitter and receiver being 30m and 1m respectively.
Examples
CNSCC.405: Digital Signal Processing
2. Consider an indoor wireless LAN with fc = 900 MHz, cells of radius 100 m, and nondirectional antennas. Under the free-space path loss model, what transmit power is required at the access point in order for all terminals within the cell to receive a minimum power of 10µW? How does this change if the system frequency is 5 GHz?
Pt = 43.9 kW = 16.42 dBW
Pt = 1.45 W = 1.61 dBW
Pr = -24.62dBm
Pr = -64.52dBm
16.99 dBw, 46.99 dBm
Pr = -33.47 dBw, -113.47 dBw

## Slide 26: Methods used to overcome Fading
Diversity
CNSCC.405: Digital Signal Processing

## Slide 27: Diversity
Diversity is a powerful communication technique that provides wireless link improvements at relatively low cost.
It provides two or more inputs at the receiver such that fading phenomenon among these inputs are uncorrelated.
If one radio path undergoes deep fading another independent path may have a strong signal at that input.
Diversity exploits the random nature of radio propagation by finding independent signal path for communication.
These independent paths are highly uncorrelated.
CNSCC.405: Digital Signal Processing

## Slide 28: Need of Diversity
Diversity scheme is needed in wireless communication because if one path of radio signal undergoes a deep fading then another independent path may have a strong signal.
CNSCC.405: Digital Signal Processing

## Slide 29: Diversity Techniques
Following are the different diversity techniques:
CNSCC.405: Digital Signal Processing

## Slide 30: Space diversity
In space diversity, signal is propagated over various propagation paths.
It uses two or more antennas to receive the signal.
Antennas are spaced enough from each other.
In urban areas, there is no clear line-of-sight between the receiver and the transmitter, so signal is reflected along multipath. So, space diversity is used to overcome this.
It is also known as Antenna diversity.
In wired transmission, it is done by transmitting using multiple wires.
CNSCC.405: Digital Signal Processing

## Slide 31: Space diversity
CNSCC.405: Digital Signal Processing

## Slide 32: Time diversity
In this form, multiple version of same signal are transmitted at different time instant.
Same signal is transmitted various time.
Message is spread in different time intervals which avoids the error burst.
It repeatedly transmits information at time spacing that exceed the coherence time of channel.
The interval between the transmission of same data should be at least the coherence time.
Multiple repetitions of the signal will be received with independent fading conditions.
Interleaving is used to obtain time diversity in digital communication.
CNSCC.405: Digital Signal Processing

## Slide 33: What is Interleaving ?
Interleaving is a way to arrange the data in non-contiguous way to increase the performance.
The function of inter-leaver is to spread the bits out in time so that if there is a deep fade or error burst, the important bits from the block of source data are not corrupted at the same time.
CNSCC.405: Digital Signal Processing

## Slide 34: Frequency diversity
Frequency diversity is implemented by transmitted same information on more than one carrier frequency.
These carrier frequencies are uncorrelated to each other, so they don’t experience the same fading.
To make them least correlated, these carrier frequencies are separated by more than the coherence bandwidth of the channel.
CNSCC.405: Digital Signal Processing

## Slide 35: Frequency diversity
Frequency Hopping Spread Spectrum (FHSS) is a special case of frequency diversity.
OFDM modulation and access technique exploit the frequency diversity.
This can be achieved by providing simultaneous modulation signals with error control coding across a large bandwidth.
If a particular frequency undergoes a fade, the composite signal will still be demodulated.
CNSCC.405: Digital Signal Processing

## Slide 36: Polarization diversity
Multiple versions of a signal are transmitted and received using antennas with different polarization.
Antennas can be either horizontal or Vertically polarized.
The antennas take advantage of multipath propagation characteristics to receive separate uncorrelated signals.
SNR is improved by up to 12 dB even in line-of-sight channel.
CNSCC.405: Digital Signal Processing